## Slide 1
SEG800 · DIGITAL SIGNAL PROCESSING
Comb Filters
Delay as a Spectral Tool
Theory · Implementation · MATLAB Evidence
x[n] + x[n−D] → repeated peaks and notches
Group #____ · Member 1 · Member 2 · Member 3

## Slide 2
SEG800 · COMB FILTERS
A Delayed Copy Creates the Filter's "Teeth"
A comb filter combines a signal with a delayed version of itself. The phase relationship between the original and delayed copy determines whether each frequency is reinforced or cancelled.
In Phase → Reinforcement
Peaks in the frequency response
Out of Phase → Cancellation
Notches (deep nulls) in the response

## Slide 3
SEG800 · COMB FILTERS
Feedforward Creates Regularly Spaced Peaks and Notches
Feedforward Comb Filter
Direct path
Immediate passthrough to sum
Delayed path
Delay D then scale by a
Summation
Direct + delayed → y[n]
Input signal
x[n] enters the filter
The direct and delayed paths sum at the output, producing periodic peaks and notches.
y[n] = x[n] + a · x[n−D]
Two Signal Paths
Direct path x[n] and delayed path with gain a and delay D samples
FIR Structure
Finite impulse response — inherently stable, no feedback loop

## Slide 4
SEG800 · COMB FILTERS
Feedback Sharpens the Repeated Resonances
Input Signal
x[n] enters the filter
Summation Node
Sum x[n] and a·y[n−D]
Output
Produce y[n] result
Delay & Scale
Delay by D and scale by a
The delayed output feeds back to the input, reinforcing resonant peaks with each pass.
y[n] = x[n] + a · y[n−D]
Recursive Path
The delayed output is returned to the input. Each pass reinforces the next, creating narrower and stronger resonant peaks.
IIR · Stability Condition
Infinite impulse response. Requires |a| < 1 to remain stable.

## Slide 5
SEG800 · COMB FILTERS
Delay Sets the Spacing Between Every Tooth
200 Hz
Tooth Spacing Δf
Fₛ ÷ D = 8000 ÷ 40
8000
Sample Rate (Hz)
Fₛ = 8000 Hz
40
Delay (samples)
D = 40 samples
Key insight: A longer delay packs the teeth closer together. Spacing is constant across the entire frequency response: \Delta f = F_s / D.

## Slide 6
MATLAB TEST SETUP
The MATLAB Test Isolates the Effect of the Delay
A simple two-tone signal makes attenuation and resonance easy to observe and verify.
Input Signal
300 Hz + 400 Hz two-tone test signal
Sample Rate
8000 Hz sampling frequency
Delay
40 samples → 5 ms delay
Feedforward Gain
a = 1.0 for FIR comb filter
Feedback Gain
a = 0.7 for IIR comb filter
Expected tooth spacing: Δf = 200 Hz

## Slide 7
MATLAB RESULTS · INPUT
The Input Contains Only Two Known Frequencies
The clean two-tone input provides a controlled baseline. Any spectral changes in the output are caused entirely by the comb filter — no other frequency content is present to obscure the result.
300 Hz
Larger amplitude component
400 Hz
Smaller amplitude component

## Slide 8
MATLAB RESULTS · TIME DOMAIN
A 5 ms Delay Is Visible Within the Short Time Window
Delay Calculation
40 samples ÷ 8000 samples/s = 5 ms
Interpretation
Each delayed copy shifts the waveform by one quarter of the 20 ms view window — clearly visible in the time-domain plot.

## Slide 9
MATLAB RESULTS · FREQUENCY RESPONSE
Both Responses Repeat Every 200 Hz — But With Different Shapes
Feedforward (FIR)
Broad peaks and deep notches. The direct and delayed signals interfere cleanly, producing wide, symmetric lobes.
Feedback (IIR)
Narrow, stronger resonant peaks. Recursion amplifies specific frequencies, sharpening each tooth.
Both structures share the same periodicity: Δf ≈ 200 Hz

## Slide 10
MATLAB RESULTS · SPECTRAL OUTPUT
The Spectra Connect Each Output Back to the Theory
300 Hz Behavior
Sits near a feedforward notch — attenuated in the FIR output. Feedback emphasizes resonant locations, altering relative amplitudes.
Key Takeaway
Both structures confirm Δf = 200 Hz spacing. Delay alone controls tooth placement; feedback controls peak sharpness.
Feedforward Output
Feedback Output