## Slide 1
WPA3 & Enhanced Wi-Fi Security

## Slide 2
Lecture Overview
What We'll Cover Today
This lecture builds wireless security knowledge progressively — from the fundamental problem of open-air transmission, through decades of encryption evolution, to the cryptographic architecture of WPA3. By the end, you won't just memorize WPA3's features; you'll understand why each one matters.
Why Wireless Is Inherently Insecure
The physics of wireless transmission and the threat landscape
WEP → WPA → WPA2 Evolution
How each standard failed, improved, and why it matters
WPA3 Architecture in Depth
SAE, forward secrecy, 192-bit enterprise mode, and PMF
Real-World Deployment & the Future
Organizations, migration challenges, and emerging threats

## Slide 3
SLIDE 1
Why Wireless Security Matters
Unlike wired networks — where an attacker must physically tap a cable — wireless signals travel through the air in every direction. Anyone within radio range can attempt to listen, capture packets, impersonate devices, or launch active attacks. The medium itself is fundamentally open. All security must come from encryption and authentication, not physical access control.
The Threat Is Physical Reality
An attacker sitting in a parking lot two cars from your building can intercept wireless traffic without ever setting foot inside. No badge. No lock to pick. Just a laptop and an antenna.
What an Attacker Can Attempt
Eavesdropping — passively reading unencrypted packets
Packet capture — collecting traffic for offline analysis
Device impersonation — spoofing a legitimate access point
Active injection — inserting or modifying frames in transit
Denial of service — flooding the wireless channel

## Slide 4
SLIDE 2
The Evolution of Wi-Fi
The IEEE 802.11 standard family began in 1997 and has been updated continuously ever since. As raw speeds increased, the data flowing across wireless networks grew far more sensitive — and attackers gained increasingly powerful hardware and software to exploit weaknesses.
1
1997 — 802.11
2 Mbps. Mainly email and basic file sharing. Security was an afterthought.
2
1999 — 802.11b
11 Mbps. Mass adoption begins. WEP introduced as the first security layer.
3
2003–2009 — 802.11g/n
54–600 Mbps. WPA and WPA2 introduced. Cloud apps emerge on wireless.
4
2013–2019 — 802.11ac/ax
Gigabit wireless. Healthcare records, financial transactions, and industrial control traffic now travel over Wi-Fi.
5
2024+ — Wi-Fi 7
Multi-gigabit. WPA3 required. Zero-trust and AI-managed radios on the horizon.
Key insight: Security standards have always lagged behind speed standards — and attackers exploit every gap.

## Slide 5
SLIDE 3
Why Do We Need Encryption?
Imagine two people having a loud conversation in a crowded coffee shop. Every person within earshot can hear every word. Wireless networking works exactly the same way. Without encryption, packets carrying passwords, files, and session tokens are fully readable by anyone monitoring the channel nearby.
Without Encryption
Passwords captured in plaintext
Confidential documents exposed
Active sessions hijacked mid-flow
User identity revealed
A payroll spreadsheet sent over open Wi-Fi is visible to any nearby observer running a packet capture tool — no special skills required.
With Encryption
Encryption converts readable plaintext into ciphertext — a scrambled form that appears as random noise to anyone without the correct cryptographic key.
Even if an attacker captures every packet on the wire, they see only meaningless data. The original information can only be recovered by a party that holds the proper key.

## Slide 6
SLIDE 4
The CIA Triad Applied to Wireless
The three pillars of information security — Confidentiality, Integrity, and Availability — map directly onto the threats that wireless networks face. Wireless encryption is not just about keeping data secret; it must address all three pillars simultaneously.
Confidentiality
Only authorized, authenticated users can read the data in transit. Encryption ensures intercepted packets reveal nothing meaningful to an eavesdropper.
Integrity
Data must arrive exactly as it was sent. Cryptographic integrity checks (like CCMP's CBC-MAC) detect any modification made to packets in transit.
Availability
Reliable authentication prevents unauthorized users from associating with the network and consuming bandwidth, degrading service for legitimate users.
💬 Discussion prompt: Which pillar of the CIA Triad is most directly threatened by an open, unencrypted Wi-Fi network — and why?

## Slide 7
SLIDE 5
WEP: The First Attempt at Wireless Encryption
Wired Equivalent Privacy (WEP) was ratified as part of the original 802.11 standard in 1999. Its goal was to give wireless networks security equivalent to a physical wire — a reasonable ambition, but one it failed to achieve almost immediately.
How WEP Was Designed
Algorithm: RC4 stream cipher
Key lengths: 40-bit or 104-bit
Initialization Vector (IV): 24-bit, prepended to each packet
The IV was intended to randomize each packet's encryption — but at only 24 bits, the same IV values repeated after as few as 5,000–7,000 packets on a busy network.
Why It Failed Catastrophically
Repeated IVs enabled statistical key recovery
The RC4 key scheduling algorithm had exploitable biases
Tools like Aircrack-ng automated the attack
Full key recovery in under 60 seconds with enough packets
This was one of the most consequential failures in the history of wireless security.

## Slide 8
SLIDE 6
How WEP Was Broken
The attack against WEP is a textbook example of how a design flaw in a cryptographic protocol can be exploited systematically. The math behind the attack does not require brute-forcing every possible key — it requires only enough packets to observe IV reuse.
Collect IVs
Capture packets with repeated 24-bit IVs.
Statistical Analysis
Identify RC4 keystream biases from collected IVs.
Recover RC4 Key
Use mathematical attacks to derive the key.
Decrypt Traffic
Use recovered key to decrypt all network traffic.
By 2005, tools like Aircrack-ng made this attack fully automated. Sitting outside a typical small business for 10 minutes was often sufficient to recover the wireless encryption key entirely. The FMS attack (Fluhrer, Mantin, Shamir) published in 2001 formally proved WEP was cryptographically broken. The IEEE had no choice but to move on.

## Slide 9
SLIDE 7
WPA: A Temporary Fix
In 2003, the Wi-Fi Alliance introduced Wi-Fi Protected Access (WPA) as an emergency interim solution. The industry could not wait years for new hardware — millions of WEP-vulnerable access points were already deployed. WPA was designed to run on existing hardware via a firmware update.
What Changed in WPA
TKIP replaced static RC4 key use
Dynamic key rotation per session
Michael MIC added message integrity checking
802.1X authentication available for enterprise use
Per-packet key mixing to prevent IV reuse exploitation
What WPA Did Not Fix
WPA still relied on the RC4 cipher as its underlying encryption engine. TKIP improved how RC4 was used, but RC4 itself remained the algorithm — a cipher that was already showing its age.
WPA was never intended as a permanent solution. It was a bridge — buying the industry time to develop WPA2 with a fundamentally stronger cipher.

## Slide 10
SLIDE 8
TKIP Explained
The Temporal Key Integrity Protocol (TKIP) was the engineering workaround that made WPA possible without requiring new hardware. It patched the most dangerous weaknesses in WEP's use of RC4 while remaining backward compatible with older chipsets.
Per-Packet Key Mixing
Instead of using the same key for every packet, TKIP derives a unique encryption key for each individual packet. This directly prevents the IV-reuse attack that broke WEP.
Temporal Key Rotation
Session keys are rotated periodically throughout a connection. Even if an attacker captures encrypted traffic, the key they might eventually recover applies only to a small time window.
Michael MIC (Message Integrity Check)
TKIP added the "Michael" algorithm to detect packet tampering. If two modified packets arrived within one second, TKIP would terminate the session — a primitive but functional integrity mechanism.
Analogy: TKIP is like changing your house locks every hour. It's a meaningful improvement — but the house still had weak doors. The real fix required replacing the entire locking mechanism with AES.

## Slide 11
SLIDE 9
WPA2 Arrives
Released in 2004 and made mandatory for Wi-Fi certified devices in 2006, WPA2 represented the first truly secure wireless encryption standard. It discarded the compromised RC4 cipher entirely and introduced the Advanced Encryption Standard (AES) as the mandatory encryption algorithm.
RC4 Retired
The RC4 stream cipher — used in both WEP and WPA — was removed entirely from WPA2. No backward compatibility compromise.
AES Mandated
AES became the required encryption algorithm. Symmetric, block-based, and mathematically sound — AES was already trusted by governments and banks worldwide.
CCMP Replaces TKIP
Counter Mode with CBC-MAC Protocol (CCMP) replaced TKIP, providing encryption, integrity verification, and replay attack protection in a single integrated protocol.
WPA2 represented the single largest improvement in wireless encryption to date. AES remains trusted and unbroken as a cipher to this day — the vulnerabilities that eventually required WPA3 were in the authentication layer, not the encryption algorithm itself.

## Slide 12
SLIDE 10
AES and CCMP
Understanding AES and CCMP in detail is essential to understanding why WPA2 was such a dramatic improvement — and why the encryption layer itself was not the vulnerability that led to WPA3.
AES — Advanced Encryption Standard
AES is a symmetric block cipher that operates on 128-bit blocks of data. It supports three key lengths:
128-bit — Standard Wi-Fi use; 2¹²⁸ possible keys
192-bit — Government and critical infrastructure
256-bit — Highest security classification
AES is used by the U.S. government, NATO, banks, hospitals, and militaries worldwide — not just Wi-Fi.
CCMP — What It Provides
Encryption — AES in Counter Mode (CTR) scrambles payload data
Integrity — CBC-MAC generates a message authentication code to detect tampering
Replay protection — A packet counter prevents attackers from re-injecting captured packets
CCMP bundles all three security functions into a single, efficient protocol — a significant improvement over the patchwork approach of TKIP.

## Slide 13
SLIDE 11
Symmetric Encryption Refresher
Wireless networks rely primarily on symmetric encryption — a model where the same cryptographic key is used to both encrypt outgoing data and decrypt incoming data. Understanding this model is foundational to understanding how AES works in a Wi-Fi context.
Symmetric Encryption Flow
Shared Secret Key
AES encrypts plaintext → ciphertext
Access Point
Decrypts ciphertext to plaintext
Laptop
Plaintext data to send
Why Symmetric Works for Wi-Fi
Extremely fast — hardware-accelerated on modern chipsets
Low CPU and battery overhead
Well-suited for real-time, high-throughput data streams
The Core Challenge
Both parties must obtain the same key through a secure channel before communication begins. This is the fundamental problem that the handshake process — and later SAE — is designed to solve. If the key exchange is compromised, the encryption is worthless.

## Slide 14
SLIDE 12
Authentication vs. Encryption
These two concepts are frequently confused by students — and keeping them separate is critical to understanding why WPA2 was vulnerable despite using strong AES encryption.
Authentication
"Who are you?"
Authentication verifies the identity of a device or user before allowing access to the network. It answers the question: Is this entity who they claim to be?
Example: Entering your PIN at an ATM authenticates your identity to the bank's system.
Encryption
"Can anyone else read this?"
Encryption scrambles data in transit so only intended recipients can read it. It protects the content of communication — not the identity of who is communicating.
Example: The encrypted link between your browser and your bank protects your session data after authentication succeeds.
Both are necessary. Strong encryption with weak authentication is like a vault with a strong lock but an easily guessed combination — the lock itself is fine; the weakness is in how you verify who gets to use it.

## Slide 15
SLIDE 13
WPA2 Authentication: The Four-Way Handshake
The WPA2 Four-Way Handshake establishes session keys between a client device and an access point without transmitting the actual password over the air. It uses a pre-negotiated Pairwise Master Key (PMK) — derived from the password — to create unique session keys (PTK) for each connection.
AP Verify & Install
Client → SNonce+MIC
AP → ANonce
Assoc Request
The critical vulnerability: The entire handshake can be captured by a passive observer. An attacker who captures the handshake can take it offline and attempt to crack the password using a dictionary attack — without ever alerting the network. This is the core weakness WPA3 was designed to eliminate.

## Slide 16
SLIDE 14
Weaknesses of WPA2
Despite using the unbroken AES cipher, WPA2 had significant vulnerabilities in its authentication and key exchange layer. Strong encryption means very little if an attacker can bypass or brute-force the authentication process that establishes the encryption keys.
Offline Dictionary Attacks
A captured Four-Way Handshake can be taken offline and tested against millions of password candidates per second using tools like Hashcat on consumer GPU hardware. The network never sees these attempts.
Shared Pre-Shared Keys (PSK)
In Personal mode, every device on the network uses the same password. One compromised device or leaked credential exposes the entire network's traffic — past and future.
KRACK (Key Reinstallation Attack)
Discovered in 2017, KRACK exploited the handshake by forcing nonce reuse through packet replay — affecting virtually every WPA2 implementation across all vendors and operating systems.
Unprotected Management Frames
Association, authentication, and disassociation frames were sent in the clear without integrity protection, enabling spoofed deauthentication attacks that forcibly disconnect legitimate clients.

## Slide 17
SLIDE 15
Introducing WPA3
Released by the Wi-Fi Alliance in 2018, WPA3 was designed from the ground up to address every significant weakness identified in WPA2. Rather than a patch, it represents a fundamental redesign of the authentication and key exchange model.
Stronger Authentication
SAE (Simultaneous Authentication of Equals) replaces PSK-based handshake, eliminating offline dictionary attacks entirely.
Forward Secrecy
Every session generates unique keys. A future password compromise cannot decrypt previously captured traffic sessions.
Protected Management Frames
PMF is now mandatory in WPA3, protecting association, authentication, and disassociation frames from spoofing.
192-Bit Enterprise Security
An optional 192-bit security suite aligned with CNSA standards, designed for government, military, and critical infrastructure.

## Slide 18
SLIDE 16
SAE: The Dragonfly Handshake
Simultaneous Authentication of Equals (SAE), based on the Dragonfly key exchange protocol, is the most important change in WPA3. It solves the fundamental flaw of the WPA2 handshake by ensuring that the password itself is never transmitted or derivable from captured traffic.
The Core Principle
Instead of exchanging password-derived key material that an attacker can capture and test offline, SAE uses a zero-knowledge proof approach: both the client and the access point independently prove they know the password — without either party ever sending it.
Each session produces a completely unique cryptographic exchange. There is no reusable handshake to capture.
What This Eliminates
Offline dictionary attacks — no captured credential to brute-force
Online brute-force — the network can rate-limit SAE attempts
Handshake replay — each exchange is mathematically unique
KRACK-style attacks — nonce reuse is not possible in SAE's design
Even a weak password becomes significantly harder to attack under SAE — though strong passwords remain best practice.

## Slide 19
SLIDE 17
WPA2 vs. WPA3: Deep Comparison
This side-by-side comparison covers every dimension where WPA3 makes a meaningful improvement over WPA2. Use this as a reference for exam preparation and practical deployment decisions.
Dimension
WPA2
WPA3
Authentication
4-Way Handshake with PSK — offline crackable
SAE (Dragonfly) — zero-knowledge, no offline attack
Encryption
AES-128 (CCMP) mandatory
AES-128 minimum; AES-256-GCM in Enterprise mode
Forward Secrecy
Not supported — past traffic vulnerable if key leaks
Mandatory — unique keys per session
Management Frames
Optional PMF (frequently misconfigured or disabled)
Mandatory PMF — deauth spoofing prevented
Offline Attacks
Highly vulnerable — GPU cracking at billions of guesses/sec
Not possible — SAE produces no reusable handshake
Enterprise Mode
128-bit AES; 802.1X with RADIUS
192-bit CNSA-aligned suite available
IoT / Simple Devices
WPS (frequently exploited)
Wi-Fi Easy Connect (QR code-based, secure)
Password Resistance
Weak passwords easily cracked offline
SAE provides strong protection even with weak passwords

## Slide 20
SLIDE 18
Forward Secrecy
Forward secrecy is one of the most practically significant improvements WPA3 brings to everyday wireless security. It means that each session's encryption keys are generated independently — and are destroyed when the session ends. No key is ever reused, and no future key can decrypt past traffic.
Why This Matters
Under WPA2, an attacker could record encrypted wireless traffic over months or years. If they later obtained the network password — through a data breach, a disgruntled employee, or a brute-force attack — they could go back and decrypt all of that previously captured traffic retroactively.
With WPA3's forward secrecy, that recorded traffic becomes permanently undecryptable, even with the correct password.
The Safe Analogy
Imagine every email you send is locked inside a completely different physical safe, each with a unique combination known only at the moment of use and then destroyed.
Even if someone finds one combination — they open exactly one safe. Every other safe remains locked forever. One compromise does not unlock the past.
This property is especially critical for healthcare, legal, financial, and government communications carried over wireless networks.

## Slide 21
SLIDE 19
192-Bit Enterprise Security Suite
WPA3-Enterprise offers an optional 192-bit security mode aligned with the Commercial National Security Algorithm (CNSA) suite — the standard used by U.S. federal agencies for protecting classified and sensitive data.
What the 192-Bit Suite Includes
AES-256-GCM for data encryption, ECDH and ECDSA using 384-bit elliptic curves for key agreement and authentication, HMAC-SHA-384 for integrity verification. Every component is elevated to match NSA Suite B requirements.
Who Uses Enterprise Mode
Canadian federal departments, U.S. government agencies, NATO members, military networks, power grid operators, financial market infrastructure, and any organization subject to regulatory requirements mandating FIPS 140-2 or higher compliance.
Why 192 Bits vs. 128 Bits
128-bit AES is secure today against all known classical attacks. 192-bit provides a larger safety margin against future advances — including early-stage quantum computing threats — for long-lived classified data that must stay secret for decades.

## Slide 22
SLIDE 20
Protected Management Frames (PMF)
Management frames are the control messages that Wi-Fi networks use to coordinate client connections. Prior to WPA3, these frames were sent in plaintext with no authentication — making them trivial to forge.
Management Frame Types
Beacon Frames
Broadcast by APs to announce network presence and capabilities
Probe Frames
Devices request and receive network availability information
Association / Disassociation
Client joins or leaves a network formally
Deauthentication
Forces a device to disconnect from the network
Before and After PMF
Before WPA3: Attackers could send a spoofed deauthentication frame impersonating a legitimate access point. The targeted device, receiving what appeared to be a valid instruction from the network, would immediately disconnect — enabling denial-of-service attacks or forcing reconnections to a rogue AP.
With Mandatory PMF: Management frames are cryptographically signed. A device receiving a deauthentication frame can verify it genuinely originated from its authenticated access point. Spoofed frames are rejected automatically.

## Slide 23
SLIDE 21
WPA3 in Real Organizations
WPA3 is not just a theoretical improvement — its features directly address the specific security challenges faced by organizations managing complex wireless environments with diverse device types and user populations.
Hospital
Medical IoT devices (infusion pumps, patient monitors) connect alongside staff laptops and physician phones. WPA3's Easy Connect enables secure IoT onboarding. PMF protects against deauth attacks that could interrupt device communication. 192-bit mode for HIPAA-sensitive clinical data.
University
Thousands of BYOD devices from students, faculty, and guests. WPA3 SAE prevents credential theft on high-density campus networks. eduroam federation with WPA3-Enterprise provides seamless, secure roaming across institutions.
Airport
Passenger Wi-Fi, airline operations, baggage handling systems, and security communications all share physical space. WPA3 separates guest access from operational networks using forward secrecy — a passenger compromise cannot reach back-end infrastructure.
Manufacturing Plant
Industrial IoT sensors, programmable logic controllers, and operator tablets require reliable, authenticated wireless connectivity. Management frame protection prevents denial-of-service attacks that could disrupt production-critical equipment communications.

## Slide 24
SLIDE 22
Migration Challenges
Transitioning an existing network from WPA2 to WPA3 is rarely as simple as changing a configuration setting. Real-world deployments involve legacy constraints, budget realities, and organizational complexity that must be managed carefully.
Technical Barriers
Legacy devices — Older printers, IoT sensors, and embedded systems may not support WPA3 at all, even with firmware updates
Driver and firmware gaps — Many enterprise-class APs require firmware upgrades to enable WPA3; some older models cannot be upgraded
Transition/Compatibility Mode — Most deployments must run WPA2 and WPA3 simultaneously, which limits some WPA3 security benefits
Organizational Barriers
Budget cycles — Hardware refresh programs may span 3–5 years; WPA3-capable APs require capital investment
Mixed vendor environments — Different AP vendors implement WPA3 features inconsistently, particularly Enterprise mode
User education — Help desk tickets spike during transitions as devices behave unexpectedly
Testing requirements — Enterprise environments require staged rollout and compatibility testing before full deployment
Best practice: Enable WPA3 Transition Mode first, monitor for client issues over 30–60 days, then gradually disable WPA2 as legacy devices are retired.

## Slide 25
SLIDE 23
Emerging Wireless Security
WPA3 is the current standard — but the wireless security landscape is already evolving toward the next generation of challenges and solutions. Understanding these trends prepares you for what comes after WPA3.
Wi-Fi 7 (802.11be)
Multi-link operation, 46 Gbps theoretical throughput. New attack surfaces from increased complexity. WPA3 required. Security architecture evolving to match.
Zero Trust Wireless
No device is trusted by default — even on an internal Wi-Fi network. Continuous identity verification, micro-segmentation, and least-privilege access enforced per device per session.
AI-Managed Radios
Machine learning detects anomalous wireless behavior — rogue APs, unusual client patterns, and novel attack signatures — in real time, enabling automated threat response.
Certificate Authentication
Moving beyond passwords entirely — device certificates issued by enterprise PKI infrastructure authenticate clients cryptographically, eliminating credential-based attacks at the source.
Quantum-Resistant Encryption
NIST has finalized post-quantum cryptographic algorithms (CRYSTALS-Kyber, CRYSTALS-Dilithium). Future wireless standards will incorporate these to resist attacks from quantum computers.

## Slide 26
SLIDE 24
Discussion Questions & Live Demonstrations
💬 Discussion Questions
1
Why isn't AES enough by itself?
Strong encryption doesn't help if the key exchange is compromised. WPA2's authentication was crackable regardless of AES strength.
2
Would you trust public Wi-Fi if it used WPA3?
Consider: SAE protects your handshake, but what about the destination servers and the access point operator themselves?
3
Should organizations disable WPA2 entirely?
Weigh security gains against operational risk. What happens to legacy medical or industrial devices that cannot be upgraded?
🔬 Lab Demonstrations
Capture beacon frames in monitor mode using Wireshark — observe management frames in plaintext
Compare the WPA2 Four-Way Handshake to a WPA3 SAE authentication trace — note what differs
Demonstrate offline password recovery from a pre-built WPA2 handshake capture using a wordlist (lab environment only)
Enable WPA3 on a lab access point and observe how client connection behavior changes
Show how Protected Management Frames in WPA3 reject spoofed deauthentication attacks
Key takeaway: WPA3 is not just a version number — it fundamentally changes the trust model of wireless authentication. Authentication and encryption are both essential; neither alone is sufficient.